劉麗蘭中文譯成英文作品參考：

【發明名稱】簡易式充氣閥構造

【發明摘要】

一種(本項)「簡易式充氣閥構造」，主要係於一底座中央設有一通孔，通孔底面設有一PU膜片，該膜片於對應通孔之外圍處環設有至少一個孔洞，並經由高週波或模壓加工技術將膜片外周緣與底座壓合 (;)，一擠壓體設於底座上方，具受壓後可彈性回復之彈性，其內部具有一氣室空間，氣室頂部設有至少一穿孔 (;)，底部周緣則設有密封緣，且同樣經由其它加工技術結合於底座而形成一充氣閥構造(;)，藉此使該充氣閥與另一氣囊結合成為一襯墊氣囊，並可按壓此充氣閥使氣囊達到充氣之效果。

【Invention Item】 Simple Inflatable Valve Structure

【Invention Abstract】

This“ Simple Inflatable Valve Structure ” is mainly provided with a ventilate hole in the center of the base, a PU diaphragm is equipped at the bottom of the ventilate hole, and with at least one hole at the periphery of the corresponding ventilate hole. The outer periphery of the diaphragm and the base are pressed to be combined by applying high frequency or press processing techniques.

An extruder, possessing the ability of resilience after receiving pressure, is provided at the top of the base. There is a chamber space inside and at least one hole at the top of the extruder.

The bottom edge is provided with a sealing edge and is likewise joined to the base via other processing techniques to form an inflatable valve structure. Whereby the inflatable valve is combined with the other balloon to form a new gasket balloon; thus, the“ Simple Inflatable Valve Structure ”can produce the effect to inflate the balloon by pressing against the inflatable valve.