Capital

System

Capital系統

Technical Specifications

技術規格

20.10.2012

2012年10月20日

OBJECT

目的

STOCK PREPARATION EQUIPMENTS:

備料設備

FOR PRODUCE FLUTING-TEST LINER BROWN

生產開槽測試 liner brown

________________________________________________________________________________

Capital System Sri	公司									Tel電話.0039 06 8069 0424

Via F. Siacci, 25-00197 Roma 羅馬							Fax 傳真0039 06 8070 446

P. IVA 07132001004								Email電子信箱:info@capitalsystem.it

1) TECHNICAL SPECIFICATION OF THE EQUIPMENTS

設備技術規範

SECTION A) COARSE SCREENING SYSTEM

A部份)進行粗篩系統

A.1)N. 3 PRIMARY COARSE SCREEN Type SELECTIFIRE EPV 1600 HD (Beloit Centiscreen A14)

初級粗篩屏幕型式SELECTIFIRE EPV 1600 HD(Beloit Centiscreen A14)

-SERIAL NUMBER系列號碼 105/2010

-SERIAL NUMBER系列號碼 106/2010

-SERIAL NUMBER系列號碼 107/2010

( ITEM 1,ITEM 2,ITEM 3 of Packing List)包裝清單第一項,第二項,第三項

Of following technical data:技術數據如下

Production 60T/day each   生產60T/每天

Consistency range 2.0-4.0% 濃度範圍 2.4-4.0%

Inlet pressure 2.5 bar 		 進氣壓力為2.5 bar

Differential pressure 0.2-0.5 bar 差壓 0.2-0.5 bar

Sealing water pressure 4.5 bar  密封水壓 4.5 bar

Dimensions Stock’s Inlet/Outlet  庫存尺寸 進口/出口

Inlet diameter 350 mm          進口直徑  350毫米

Outlet diameter 350 mm         出口直徑 350毫米

Reject bottom outlet 100 mm     廢品底部出口 100毫米

External Basket diameter 900 mm 外部籃直徑 900毫米

Hole diameter 2 mm 			  孔直徑 2毫米

Height Basket 550 mm 		  籃高 500毫米

Internal Basket diameter 590 mm  籃內部直徑 590毫米

Hole diameter 3 mm             孔直徑 3毫米

Height Basket 550 mm			  籃高 550毫米

Motor type n.2 of 45 Kw and n.1 50 Kw triphase, 電機類型N.245千瓦和N.150千瓦三相

squirrel cage, version B5, 380 V 鼠籠，版本B5，380 V

Drive type pulleys/belts  驅動型皮帶輪/皮帶

Including  包括

Cylindrical housing 圓柱型住房

Housing inlet /outlet /rejects / dilution connections 	房屋入口/出口/拒絕/稀釋連接

Cover 覆蓋

Trap for light weight rejects   trap供重量輕的廢品

Internal trap for heavy rejects 內部trap供重量重的廢品

Special design rotor, dynamically balanced with n.4 Blades that n.2 work in the external basket and n.2 work on the internal basket

特別設計的轉子,動態的平衡與n.4刀片，在n.2外部籃工作及n.2內部籃工作

Basket with profiled holes 異形孔籃

Rotor shaft with sealing, water lubricated 轉子軸密封，水潤滑

2 SKF Roll Bearings 卷軸承

Foundation bolts地腳螺栓

Drive by pulleys and Vee-belts 經皮帶輪和V帶驅動

Motor/Screen base plate / slide rails馬達/屏幕底板/滑軌

A.2) N. 4 High Density Cleaner Type GD 200 / D2 - model as Escher Wiss

N.4高密度清潔GD型200/ D2 – 型號如Escher Wiss

-SERIAL NUMBER 系列號碼48/2010

-SERIAL NUMBER 系列號碼49/2010

-SERIAL NUMBER 系列號碼50/2010

-SERIAL NUMBER 系列號碼51/2010

( ITEM 4,ITEM 5,ITEM 6, ITEM 7 of Packing List) 包裝清單第四項,第五項,第六項

Of following technical data: 技術數據如下

Capacity each one 1.800-3.000 LITRE PER MINUTE  每分鐘每一個容量1.800-3.000公升Consistency 濃度3.0-4.5%

Inlet pressure進氣壓力1.5/3 bar

Outlet pressure出口壓力0.3 - 2 bar

Back pressure water 背壓水0.5 bar

Operation mode 操作模式continuous連續

Dimensions Stock’s Inlet/Outlet  庫存進口/出口的尺寸

Inlet diameter  進口直徑 100 mm 毫米

Outlet diameter 出口直徑 100 mm毫米

Reject bottom outlet廢品底部出口200 mm毫米

Including 包括

Housing

Head with stock tangential inlet 庫存切向入口頭

Top separation cone 頂部分離錐

Bottom separation cone 底部分離錐

Inspection sight hole 檢查觀察孔

Shaft in special steel 特殊鋼軸

Flushing and sealing 沖洗和密封

Special rotor of separation for centrifugation 特別轉子離心分離

A System of driving rotor with Motor 4 Kw -980 rpm complete with n.2 pulleis

and belts.

A系統驅動轉子電機4千瓦-980轉以N.2 pulleis的和皮帶完成。

Rotor bearing: grooved ball bearings with grease lubrication 轉子軸承：深溝球軸承及脂潤滑

Seals: bearing- labyrinth seal Supporting frame 密封：軸承迷宮密封支撐架

SECTION B) FINE SCREENING SYSTEM   B部分）細篩系統

B.1) N. 1 FINE SCREENING SYSTEM Type SELECTIFIRE SHD 700 – BLACK CLAWSON PH24

B.1）N.1細篩系統類型SELECTIFIRE SHD700 - BLACK CLAWSON PH24

-SERIAL NUMBER系列號碼101/2010

( ITEM 1 of Packing List) 包裝清單第一項

Of following technical data: 技術數據如下

Capacity容量 110 – 120 T/day 天

Consistency range濃度範圍 1.5-3.5%

Inlet pressure進氣壓力2.0-2.5 bar

Differential pressure差壓 0.2-0.5 bar

Sealing water pressure密封水壓力3-4.5 bar

Dimensions Stock’s Inlet/Outlet庫存尺寸的進口/出口

Inlet diameter 進口直徑 250 mm 毫米

Outlet diameter出口直徑 300 mm 毫米

Reject bottom outlet 廢品底部出口100 mm毫米

External Basket diameter 外部籃直徑 610 mm 毫米

Hole diameter(conical) 孔直徑（圓錐形）2,5-3 mm毫米

Height Basket 籃高600 mm毫米

Motor type馬達類型n.1 of 45 Kw -1465 rpm, triphase,

squirrel cage鼠籠, version版本 B5, 380 V

Drive type pulleys/belts 驅動型皮帶輪/皮帶

Including 包括

Cylindrical housing 圓柱型殼

Housing inlet /outlet /rejects / dilution connections  Housing入口/出口/拒絕/稀釋連接

Cover 蓋子

Trap for light weight rejects  trap供重量輕的廢品

Internal trap for heavy rejects  內部trap供重量重的廢品

Special design rotor, dynamically balanced with n.4 Blades

特殊設計的轉子，以N.4刀片動態的平衡

Basket with profiled holes異形孔的籃

Rotor shaft with sealing, water lubricated 轉子軸密封，水潤滑

2 SKF Roll Bearings輥軸承

Foundation bolts 地腳螺栓

Drive by pulleys and Vee-belts  經皮帶輪和V帶驅動

Motor/Screen base plate / slide rails 馬達/屏幕底板/滑軌

B.2) N. 1 FINE SCREENING SYSTEM Type SELECTIFIRE SHD 400 - Black Clawson PH12

N.1細篩系統類型SELECTIFIRE SHD400 - Black Clawson PH12

-SERIAL NUMBER 系列號碼103/2010

( ITEM 2 of Packing List)  包裝清單第二項

Of following technical data:技術數據如下

Capacity容量 50 – 60 T/day 天

Consistency range 濃度範圍 1.5-3.5%

Inlet pressure進氣壓力 2.0-2.5 bar

Differential pressure差壓 0.2-0.5 bar

Sealing water pressure密封水壓力 3-4.5 bar

Dimensions Stock’s Inlet/Outlet 庫存尺寸的進口/出口

Inlet diameter  進氣口直徑 200 mm 毫米

Outlet diameter 出口直徑 200 mm 毫米

Reject bottom outlet 廢品底孔100 mm 毫米

External Basket diameter外部籃直徑610 mm毫米

Hole diameter(conical) 孔直徑（圓錐形）2,5-3 mm毫米

Height Basket籃高 320 mm毫米

Motor type 馬達形式n.1 of 30 Kw -1450 rpm, triphase,

squirrel cage鼠龍, version 版本B5, 380 V

Drive type pulleys/belts驅動型皮帶輪/皮帶

Including 包括

Cylindrical housing圓柱型 housing

Housing inlet /outlet /rejects / dilution connections housing入口/出口/拒絕/稀釋連接

Cover蓋子

Trap for light weight rejects  trap供重量輕的廢品

Internal trap for heavy rejects 內部trap供重量重的廢品

Special design rotor, dynamically balanced with n.4 Blades

特殊設計的轉子，以N.4刀片動態的平衡

Basket with profiled holes 異形孔的籃

Rotor shaft with sealing, water lubricated轉子軸密封，水潤滑

2 SKF Roll Bearings 輥軸承

Foundation bolts地腳螺栓

Drive by pulleys and Vee-belts經皮帶輪和V帶驅動

Motor/Screen base plate / slide rails馬達/屏幕底板/滑軌

B.3) N. 1 FINE SCREENING SYSTEM Type SCREEN SHD 400 - NUOVA OMMA

N.1細篩系統類型屏幕SHD400 - NUOVA OMMA

- SERIAL NUMBER 系列號碼104/2010

( ITEM 3 of Packing List) 包裝清單第三項

Of following technical data: 技術數據如下

CAPACITY容量 70-80 T/DAY天

Consistency range 濃度範圍1.5-3.5%

Inlet pressure進氣壓力2.0 – 2.5 bar

Differential pressure差壓0.2-0.5 bar

Sealing water pressure密封水壓力3.0-4.0 bar

Dimensions Stock’s Inlet/Outlet 庫存進口/出口的尺寸

Inlet diameter 進氣口直徑 300 mm毫米

Outlet diameter 出口直徑 300 mm毫米

Reject bottom outlet 廢品底孔100 mm毫米

External Basket diameter 外部籃直徑700 mm毫米

Height Basket 籃高600 mm毫米

Basket type Holes籃式孔

Hole diameter 孔直徑2,0 mm毫米

Motor type馬達形式 n.1 of 15 Kw -1450 rpm, triphase,

squirrel cage鼠籠, version 版本B5, 380 V

Drive type pulleys/belts驅動型皮帶輪/皮帶

Including 包括

Cylindrical housing 圓柱形housing

Housing inlet /outlet /rejects / dilution connections  housing入口/出口/拒絕/稀釋連接

Cover 蓋子

Trap for light weight rejects  trap供重量輕的廢品

Internal trap for heavy rejects 內部trap供重量重的廢品

Special design rotor, dynamically balanced with Blades

特殊設計的轉子，以N.4刀片動態的平衡

Basket with profiled slots異形孔的籃

Rotor shaft with sealing, water lubricated 轉子軸密封，水潤滑

2 SKF Roll Bearings 輥軸承

Foundation bolts 地腳螺栓

Drive by pulleys and Vee-belts 經皮帶輪和V帶驅動

Motor/Screen base plate / slide rails馬達/屏幕底板/滑軌

Safety guards 安全監視

B.4) N. 1 FRACTIONATORS OF FIBERS Type FHD1100 - SUNDS DEFIBRATOR

N.1分餾纖維類型FHD1100 - SUNDS磨機

- SERIAL NUMBER 系統號碼108/2010

( ITEM 4 of Packing List) 包裝清單第四項

Of following technical data: 技術數據如下

CAPACITY 容量60-70 T/DAY 天

Consistency range 濃度範圍1.5-3.5%

Inlet pressure進氣壓力2.5 - 3 bar

Differential pressure差壓0.3-0.5 bar

Sealing water pressure密封水壓力3.0-4.0 bar

Dimensions Stock’s Inlet/Outlet  庫存進口/出口的尺寸

Inlet diameter 進氣口直徑150 mm毫米

Outlet diameter出口直徑150 mm毫米

Reject bottom outlet廢品底孔80 mm毫米

External Basket diameter外部籃直徑500 mm毫米

Height Basket籃高 400 mm毫米

Basket type Wedge wire slots籃式楔形絲槽

Slots size插槽大小0,4 mm毫米

Motor type 馬達形式n.1 of 50 Kw - 970 rpm, triphase,

squirrel cage鼠籠, version 版本B5, 380 V

Drive type pulleys/belts驅動型皮帶輪/皮帶

Including包括

Cylindrical housing圓柱形housing

Housing inlet /outlet /rejects / dilution connections housing入口/出口/拒絕/稀釋連接

Cover 蓋子

Trap for light weight rejects  trap供重量輕的廢品

Internal trap for heavy rejects內部trap供重量重的廢品

Special design rotor, dynamically balanced with Blades

特殊設計的轉子，動態均衡的刀片

Basket with profiled slots異形孔的籃

Rotor shaft with sealing, water lubricated轉子軸密封，水潤滑

2 SKF Roll Bearings輥軸承

Foundation bolts地腳螺栓

Drive by pulleys and Vee-belts經皮帶輪和V帶驅動

Motor/Screen base plate / slide rails 馬達/屏幕底板/滑軌

Safety guards安全監視

SECTION C) DISPERGER   C部分）分散

ESCHERWISS PLANT CAPACITY 工廠產能80-90T/DAY天

C.1) N. 1 UPPER SCREW

C.1）N.1上部螺旋式

- SERIAL NUMBER 系列號碼201/2010

( ITEM 5 of Packing List) 包裝清單第五項

Of following technical data: 技術數據如下

Consistency range濃度範圍 15-25%

Dimensions 尺寸

Screw diameter 螺桿直徑250 mm 毫米

Vat diameter 缸徑300 mm毫米

Inlet Diameter 進氣口徑200 mm毫米

Outlet Diameter出口直徑200 mm毫米

Motor type 馬達型式n.1 of 4 Kw - 2910 rpm, triphase,

squirrel cage鼠籠, version版本 B5, 380 V

Drive type pulleys/belts 驅動型皮帶輪/皮帶

Including包括

Cylindrical housing 圓柱型housing

Cover 蓋子

Vat in Stainless steel 不銹鋼缸

Screw in Stainless steel 不銹鋼螺絲

Special design rotor, dynamically balanced with helical Blades

特殊設計的轉子，動態的平衡帶螺旋葉片

Rotor shaft with sealing, water lubricated轉子軸密封，水潤滑

2 SKF Roll Bearings 輥軸承

Foundation bolts地腳螺栓

Drive by pulleys and Vee-belts 經皮帶輪和V帶驅動

Motor/Screen base plate / slide rails 馬達/屏幕底板/滑軌

C.2) N. 1 LOWER SCREW - SPEED HEATER

C.2）N.1下方的螺絲 - SPEED取暖器

- SERIAL NUMBER系列號碼201/2010

( ITEM 6 of Packing List) 包裝清單第六項

Of following technical data: 技術數據如下

Consistency range 濃度範圍15-25%

Dimensions 尺寸

Screw diameter 螺桿直徑500 mm 毫米

Vat diameter缸徑600 mm毫米

Inlet Diameter Square Flange 進氣口徑方形輪緣

Outlet Diameter Square Flange 出氣口徑方形輪緣

Motor type 馬達型式n.1 of 50 Kw - 1570 rpm, triphase,

squirrel cage鼠籠, version 版本B3, 380 V

Drive type Gear reducer, Pinion and chains驅動型齒輪減速機，齒輪和鏈條

Including包括

Cylindrical housing圓柱型housing

Cover蓋子

Vat in Stainless steel不銹鋼缸

Screw in Stainless steel不銹鋼螺絲

Special design rotor, dynamically balanced with helical Blades

特殊設計的轉子動態的平衡，帶螺旋葉片

Rotor shaft with sealing, water lubricated轉子軸密封，水潤滑

2 SKF Roll Bearings輥軸承

Foundation bolts地腳螺栓

Drive by Gear reducer, pinions and chains驅動齒輪減速機，齒輪和鏈條

Motor/Screen base plate / slide rails馬達/屏幕底板/滑軌

C.3) N. 1 THICKENER FOR DISPERGER  N.1增稠劑分散

(SERIAL NUMBER系列號碼 201/2010)

Complete of : 完成的

- FRAME AND ROLLS 機架和滾輪( ITEM 7 of Packing List) 包裝清單第七項

- RUBBER PRESSES橡膠機( ITEM 8 of Packing List) 包裝清單第八項

- TORPRESS ( ITEM 9 of Packing List) 包裝清單第九項

- GEAR MOTOR WITH DRIVE AND JOINT齒輪馬達驅動器和接頭

( ITEM 10 of Packing List) 包裝清單第十項

Of following technical data: 技術數據如下

Inlet Consistency range進口濃度範圍2-3%

Outlet Consistency range出口濃度範圍15-25 %

Dimensions 尺寸

Drum Thickener diameter轉鼓濃縮機直徑1250 mm毫米

Width of Drum Thickener轉鼓濃縮機的寬度1500 mm毫米

Diameter of Rubber presses橡膠機直徑400 mm毫米

Diameter of Torpress Torpress直徑 300 mm毫米

Motor type馬達型式 n.1 of 7,5 Kw - 1450 rpm, triphase,

squirrel cage鼠籠, version版本 B3, 380 V

Drive type Gear reducer and Joint驅動型齒輪減速機和接頭

Including包括

FRAMES AND ROLLS 機架和滾輪

The Frame is made with : 機架是用

-N.1 Drum diameter 1250 mm and size 1500 mm in Stainless Steel and complete of Cylindrical housing with bearings

N.1鼓直徑1250毫米，尺寸1500毫米的不銹鋼和完整的軸承圓柱housing

- N.1 Set of Frame made in Middle painted steel which are the support of all rolls and drum - N.1 Set Of Guide Rolls: N.1組機架由中東彩塗鋼板，有軋輥和感光鼓的支持 - N.1組的滾輪指南： diameter 370 and width 1600 mm complete of supports, 直徑370寬度1600毫米完整支持，

bearings SKF lubricated by grease and realized in the following way :

SKF軸承採用油脂潤滑，並通過以下方式實現：

. Shell in steel UNI Fe52St in high thickness 殼牌鋼的UNI Fe52St在高厚度

. Pivots made in steel 38NCD4 鋼38NCD4支點

. Rubber Cover type Diamantite sp.15 mm and hardness 0-1 P.J 橡膠蓋型Diamantite sp.15毫米，硬度0-1 PJ

. Dynamic Balancing for a speed of 200 m/min G=2,5. 動平衡的速度200米/分鐘G =2,5。

. Supports and bearings SKF 支持及SKF軸承

- N.1 Stretcher complete with arms in middle painted steel and torpress to move the stretcher

N.1延伸器完成以桿中間彩塗鋼板和torpress完整移動到延伸器

- N.1 Automatic and pneumatic guide roll   N.1自動和氣動導輥

RUBBER PRESSES 橡膠機

The Rubber press is made in diameter 400 and width 1600 mm complete of supports, 橡膠按直徑400寬度1600毫米完整的支持，

bearings SKF lubricated by grease and realized in the following way :

SKF軸承採用油脂潤滑，並通過以下方式實現：

. Shell in steel UNI Fe52St in high thickness 殼牌鋼的UNI Fe52St在高厚度

. Pivots made in steel 38NCD4 鋼38NCD4支點

. Rubber Cover type Diamantite sp.15 mm and hardness 0-1 P.J 橡膠蓋型Diamantite sp.15毫米，硬度0-1 PJ

. Dynamic Balancing for a speed of 200 m/min G=2,5. 動平衡的速度200米/分鐘G =2,5。

. Supports and bearings SKF 支持及SKF軸承

TORPRESS

The System Torpress is including the particular air springs that are used for to move the Rubber Press against the Drum

Torpress系統包括特定的空氣彈簧用於移動橡膠按對鼓

In the system are included the arms made in middle painted steel complete of support and bearings.

在該系統中都包含在中間畫完整的支持和軸承鋼製成的桿。

GEAR MOTOR WITH DRIVE AND JOINT齒輪電機驅動器和接頭

The System include the Gear Reducer of an appropriate ratio and the Electrical Motor of 7,5 Kw

該系統包括一個適當的比例和7,5千瓦的電氣馬達的齒輪減速器

- 1450 rpm, triphase, version B3, 380 V .

In the shaft of Gear reducer is mounted the semi joint to be connected to the shaft of the cylinder. 在軸的齒輪減速機安裝要連接到氣缸的軸的半關節。

2 Conical Refiners type錐形煉油類型 as Escher Wiss R3

consistency max 最大濃度6%

production max 最大產能100 - 120 ton/day 天

throughput max 吞吐量最大1500 l./ min 分

1 Disperger type分散型 as Escher Wiss HD3

production max最大產能. 120 - 150

consistency濃度 25 - 30 %

1 Horizontal Screw - part of Hot Treatment Plant

1臥式螺旋 - 熱水處理廠的一部分

1 Thickener Drum 增稠劑鼓

diameter直徑1250 x 2500

wires in st. st. ST電線